## Slide 1: Compact X-Ray Free-Electron LASER
What David did on his summer vacation…

## Slide 2
https://www.youtube.com/watch?v=HLF2sv78fiQ&t=4s

## Slide 3
3
Science with Ultrafast & Coherent X-rays
Catalysis & Renewable Energy
Quantum Materials
Next-Generation Electronics
Biomolecular Movies
(Pharmaceutics, Photosynthesis,..)
Advanced Imaging (Medical,
Forensics,
Cultural Heritage,…)
Matter in Extreme Conditions

## Slide 5
Soft X-ray suite (CXFEL)
Hard X-ray suite (CXLS)
5
Beus Compact X-ray FEL (CXFEL) Labs at ASU
Biodesign C building (2018) ~12,000 ft2 customized space for CXFEL labs
Compact X-ray sources:
Replace periodic “undulator” magnets with intense ultrashort light pulses
l
Image source: Wikipedia, LibreTexts
Shorter wavelength  reduced electron beam energy
LightConversion Yb:KGW
1030/515/258 nm
1.5 mJ/shot at 1030
0.15 mJ/shot at 258
200 fs
1 kHz
ASU-TibaRay
Photoinjector
9.3 GHz
1 kHz
120 MV/m
4.5 cell
4 MeV energy
200 pC
1 ps
Scandinova solid-state modulators, L3Harris klystrons
9.3 GHz
6 MW for 1 µs at 1 kHz
<100 ppm stability
Trumpf Yb:YAG
1030 nm
200 mJ/shot
1 ps
1 kHz
M2 = 1.2
X-ray Chambers
108 photons/shot
1-40 keV
300 fs
1 kHz
CXLS length is 10 m from photoinjector to beam dump
Final focus and interaction point
Diagnostics and matching quad triplets
chicane
compressor
Electron diffraction
TibaRay linacs
9.3 GHz standing wave
1 kHz
25-30 MV/m
20 cells/section (3 sections)
30 MeV final energy
X-ray Phase Contrast Imaging
Pump Laser
Beam Dump